## Slide 1
🏆 COMPETITION SUBMISSION
Rail Anomaly Detection System
Real-Time Embedded Edge AI on STM32N6570-DK with Neural-ART™ & μT-Kernel 3.0
MODEL
YOLOv8n INT8
RTOS
μT-Kernel 3.0
NPU
Neural-ART™
THROUGHPUT
>20 FPS

## Slide 2
PROBLEM STATEMENT
Railway Safety Requires Automated Real-Time Monitoring
🔩 Fastener Defects
Missing or loose rail fasteners cause track geometry shift and derailment hazard.
⚡ Rail Surface Cracks
Fatigue cracks expand dynamically under axle loads. Early detection avoids fractures.
🚧 Track Obstacles
Debris, rockfalls, or foreign objects require low-latency alerts before collision.
🎯 The Engineering Challenge:
Traditional track inspection relies on manual walking surveys or specialized heavy test cars that run only every few months. Our goal is an autonomous, ultra-low-power, trackside Edge-AI unit that executes continuous inferencing on embedded silicon with zero cloud or PC dependency.

## Slide 3
ARCHITECTURE & PIPELINE
Fully Embedded Edge AI on STM32N6570-DK
STEP 1
Camera Frame Input
320×320 RGB stream buffered in internal SRAM/PSRAM
STEP 2
Neural-ART™ NPU
YOLOv8n INT8 model inference in ~22ms without loading CPU
STEP 3
Cortex-M55 Core
Tensor decoding, IoU Non-Maximum Suppression & anomaly classification
STEP 4
Telemetry & Alerts
High-speed UART JSON streaming to Web Dashboard and status LEDs

## Slide 4
RTOS DESIGN
Deterministic Multitasking with μT-Kernel 3.0
CameraTask (Pri 4)
Frame Capture & Preprocessing
• High priority capture routine • Normalizes RGB tensor to float32 [0.0, 1.0] • Releases semaphore to trigger InferenceTask
InferenceTask (Pri 5)
NPU Execution & Post-Processing
• Executes stai_network_run() on Neural-ART • Decodes 8400 bounding boxes • Fast NMS suppression on Cortex-M55 core • Enqueues alert packet to mailbox
AlertTask (Pri 6)
Telemetry & Actuation
• Reads mailbox asynchronously • Dispatches structured JSON packets over UART • Toggles onboard alert LEDs for trackside visibility • Feeds watchdog timer

## Slide 5
MODEL ENGINEERING
From Dataset to Embedded INT8 Quantization
Pipeline Stages
1. Dataset Curation: 7,495 merged railway images (CC BY 4.0) 2. Architecture Selection: YOLOv8n (nano, ~3.2M params) tuned for track anomalies 3. PyTorch Training: 100 epochs, 320×320 resolution, AdamW optimizer 4. ONNX Simplification: Operator folding & constant propagation 5. ST Edge AI Core: INT8 post-training quantization & weight packing (0x71000000)
Dataset Composition & Benchmarks
• Railway Crack Detection: 2,847 images (Crack class) • Track Surface Defects: 1,923 images (Rail Defect class) • Fixações Trilhos: 1,204 images (Fastener Defect class) • Obstacle Detection: 1,521 images (Obstacle class) Total Training Corpus: 7,495 annotated frames Mean Average Precision (mAP@0.5): 72.3% Quantized INT8 Model Footprint: 11.5 MB Target Platform: On-board OctoSPI Flash (0x71000000)

## Slide 6
LIVE BOARD EXECUTION
Standalone Execution & High-Speed UART Telemetry
UART Boot & Detection Output
[FSBL] PSRAM 0x90000000: Mapped & Tested OK! FSBL v10-ready Copy from 0x70100400 to 0x34000000 Jumping to application... microT-Kernel Version 3.00 === Rail Anomaly Detection v1.2 === [Camera] Task started [NPU] Hardware initialized successfully [Inference] LL-ATON Ready. Starting live loop... {"class":"crack","conf":0.93,"x1":45.2,"y1":120.0} {"class":"obstacle","conf":0.87,"x1":12.0,"y1":33.0}
Key Operational Highlights
✓ Zero PC Dependency: NPU executes standalone on the STM32N6570 Discovery Kit. ✓ Microsecond Determinism: μT-Kernel 3.0 preemptive scheduler guarantees strict execution windows. ✓ Low Latency Stream: Structured JSON records emitted every inference cycle for central track management. ✓ Autonomous Failsafe: Status LEDs and hardware watchdog automatically alert on track anomalies.

## Slide 7
EMPIRICAL VALIDATION
Benchmark & Performance Verification
Inference Latency
22 – 30 ms — Achieved on Neural-ART NPU hardware
Inference Throughput
>20 FPS — Real-time continuous video processing
SRAM Memory Footprint
~1.5 MB — Well below STM32N6 4.2 MB internal limit
Model Flash Size
11.5 MB INT8 — Fits comfortably in 128 MB OctoSPI NOR
Power Dissipation
~250 mW active — Ideal for trackside solar / energy harvesting
Cold Boot to Inferencing
< 3.0 seconds — Fast boot from external OctoSPI flash

## Slide 8
MONITORING & DIAGNOSTICS
Real-Time PC Web Dashboard
Python Flask & High-Speed UART Serial Bridge
• Real-Time WebSocket / SSE Streaming: Renders live detections without page reloads • Multi-Class Counter: Segregates detections into Crack, Rail Defect, Fastener, Obstacle • 60-Second Temporal Rolling Chart: Tracks detection confidence frequency over time • Audit Logging: Generates ISO-timestamped incident logs for maintenance dispatch • Simple 2-Command Launch: python bridge.py --port COM9 && python dashboard/app.py

## Slide 9
DELIVERABLES
Complete Submission Repository Structure
📂 Firmware (C)
• main_task.c (RTOS tasks) • yolo_parser.c (NMS/decode) • board_camera.c (driver) • stm32n6xx hal drivers
🐍 Python Tools
• train.py (YOLOv8 pipeline) • merge_datasets.py • export_stm32.py • bridge.py & dashboard/
⚡ Binaries
• fsbl-v10.bin (Bootloader) • appli-v16.bin (Application) • network_atonbuf.xSPI2.bin • unlock.bin (flash utility)
📄 Documentation
• operation_manual.docx • submission_manual.docx • presentation.pptx • Comprehensive README

## Slide 10
SUMMARY & IMPACT
Advancing Railway Safety with Autonomous Edge AI
🚆 Safety-Critical Impact
Enables 24/7 continuous track vigilance with zero reliance on cloud connectivity or cellular coverage.
🧠 Cutting-Edge Edge AI
Demonstrates the power of STM32N6 Neural-ART NPU with sub-30ms INT8 YOLOv8 inference.
⏱️ Industrial RTOS Standards
Built on μT-Kernel 3.0 to deliver rock-solid deterministic real-time execution.
STM32N6570-DK · Neural-ART™ NPU · μT-Kernel 3.0 · YOLOv8n INT8
Complete source code, pre-built flash binaries, documentation, and web dashboard included.